Data Processing
ADD, ADC, SUB, SBC, RSB
op{S}{cond} {Rd,} Rn, Operand2
op{cond} {Rd,} Rn, #imm12	; ADD and SUB only
S Is an optional suffix. If S is specified, the condition code flags are updated on the result of the operation, see Conditional execution.
cond Is an optional condition code, see Conditional execution.
Rd Specifies the destination register. If Rd is omitted, the destination register is Rn.
Rn Specifies the register holding the first operand.
Operand2 Is a flexible second operand. See Flexible second operand for details of the options.
Imm12 This is any value in the range 0-4095.
AND, ORR, EOR, BIC, ORN
op{S}{cond} {Rd,} Rn, Operand2
S Is an optional suffix. If S is specified, the condition code flags are updated on the result of the operation, see Conditional execution.
cond Is an optional condition code, see Conditional execution.
Rd Specifies the destination register.
Rn Specifies the register holding the first operand.
Operand2 Is a flexible second operand. See Flexible second operand for details of the options.
ASR, LSL, LSR, ROR, RRX
op{S}{cond} Rd, Rm, Rs
op{S}{cond} Rd, Rm, #n
RRX{S}{cond} Rd, Rm
S Is an optional suffix. If S is specified, the condition code flags are updated on the result of the operation, see Conditional execution.
Rd Specifies the destination register.
Rm Specifies the register holding the value to be shifted.
Rs Specifies the register holding the shift length to apply to the value in Rm. Only the least significant byte is used and can be in the range 0 to 255.
n Specifies the shift length. The range of shift length depends on the instruction:
ASR shift length from 1 to 32
LSL shift length from 0 to 31
LSR shift length from 1 to 32
ROR shift length from 1 to 31.
CLZ
CLZ{cond} Rd, Rm
cond Is an optional condition code, see Conditional execution.
Rd Specifies the destination register.
Rm Specifies the operand register.
CMP, CMN
CMP{cond} Rn, Operand2
CMN{cond} Rn, Operand2
cond Is an optional condition code, see Conditional execution.
Rn Specifies the register holding the first operand.
Operand2 Is a flexible second operand. See Flexible second operand for details of the options.
MOV, MVN
MOV{S}{cond} Rd, Operand2
MOV{cond} Rd, #imm16
MVN{S}{cond} Rd, Operand2
S Is an optional suffix. If S is specified, the condition code flags are updated on the result of the operation, see Conditional execution.
cond Is an optional condition code, see Conditional execution.
Rd Specifies the destination register.
Operand2 Is a flexible second operand. See Flexible second operand for details of the options.
imm16 This is any value in the range 0-65535.
MOVT
MOVT{cond} Rd, #imm16
cond Is an optional condition code, see Conditional execution.
Rd Specifies the destination register.
imm16 Is a 16-bit immediate constant.
REV, REV16, REVSH, RBIT
op{cond} Rd, Rn
cond Is an optional condition code, see Conditional execution.
Rd Specifies the destination register.
Rn Specifies the register holding the operand.
TST, TEQ
TST{cond} Rn, Operand2
TEQ{cond} Rn, Operand2
cond Is an optional condition code, see Conditional execution.
Rn Specifies the register holding the first operand.
Operand2 Is a flexible second operand. See Flexible second operand for details of the options.